## Slide 1
김정인
jikim@imguru.co.kr
강의환경 : raspberry pi 확장 보드 , ubuntu 18.04
강의 자료 공유 서버 :
ftp-server : 156.147.178.101
id : linux
passwd : 없음
강의자료 배포 : 01_day 폴더
01_day.ppt
강의 시간 : 40분 - 15 ~ 20 휴식
11시 45분 - 13시 05분

## Slide 2
module programming
kernel timer
interrupt , workqueue
Process ( task_struct )
Schedule , O(n) -> O(1) -> CFS
signal
Buddy System
Slab allocator
Vmalloc
Virtual File System
Major 번호 분기 ( register_chrdev , register_chrdev_region )
Minor 번호 분기
Major 번호 / Minor 번호 동적 생성
Device 특수 파일의 동적 생성
GPIO 제어
7 Segment 제어
모터 제어
부저 제어
LED
Sysfs 이용한 하드웨어 제어

## Slide 3
  an instance(Memory) of a running program (runnable program)

## Slide 4
  #define get_current() (current_thread_info()->task)
  #define current get_current()
  //---------------------------------------------------
  current;
  current_thread_info()->task;

## Slide 5
  static inline struct thread_info *current_thread_info(void)
  {
  return (struct thread_info *)
  (current_stack_pointer & ~(THREAD_SIZE - 1));
  }
  current_thread_info();
  __get_free_pages( order = 1 );
2 pages
1
int buffer[4096];
  buffer=__get_free_pages( 2 );
0x12340000
0x12341000
0x12342000
0x12341234

## Slide 6
  static inline struct thread_info *current_thread_info(void)
  {
  return (struct thread_info *)
  (current_stack_pointer & ~(THREAD_SIZE - 1));
  }
00010010001101000001001000110100
11111111111111111110000000000000 &
----------------------------------
00010010001101000000000000000000
0001 0010 0011 0100
0x12340000
0x12340000
0x12341000
0x12342000
0x12341234

## Slide 7
  static inline struct thread_info *current_thread_info(void)
  {
  return (struct thread_info *)
  (current_stack_pointer & ~(THREAD_SIZE - 1));
  }
  current_thread_info();
  struct thread_info *p = __get_free_pages( order = 1 );

## Slide 8
0x12340000
0x12341000
0x12342000
0x12341234
thread_info.task
task_struct

## Slide 9
user
running
kernel
running
zombie
initial
(idle)
fork
ready
to run
suspended
ready
asleep
suspended
asleep
fork
return from
syscall or
interrupt
syscall,
interrupt
switch
sleep, lock
wakeup, unlock
exit
wait
swap
swap
switch
(Source : UNIX Internals)
부팅시 init 프로세스 생성
모든 프로세스는
init으로 부터 생성됨

## Slide 10
Kernel execution
process A execution
Kernel execution
Kernel execution
Kernel execution
process C execution
process B execution
process B creation
Interrupt or Trap cause change of execution modes
(Source : Magic Garden)
fork();
schedule();
interrupt
schedule();

## Slide 11
ls
ps
vi
Ready Queue
PC
SP
fetch - decode - execute
CPU의 양보 시점
1. I/O요청시 당장 실행 불가능
Wait Queue
TASK_RUNNING
TASK_INTERRUPTIBLE
PIC
irq=0x21

## Slide 12
ls
ps
calc
Ready Queue
PC
SP
fetch - decode - execute
CPU의 양보 시점
I/O요청시 당장 실행 불가능
주어진 시간(100ms)이 만료되면
Wait Queue
counter=100ms
TASK_INTERRUPTIBLE
PIC
irq=0x20
10ms
counter=100ms
counter=100ms

## Slide 13
ls
ps
calc
Ready Queue
PC
SP
fetch - decode - execute
CPU의 양보 시점
I/O요청시 당장 실행 불가능
주어진 시간(100ms)이 만료되면
Wait Queue
TASK_INTERRUPTIBLE
PIC
irq=0x20
10ms
PC
SP
PC
SP
PC
SP

## Slide 14
1세대 커널
  List와 for loop 를 이용한 방식
  Nice 값은 낮을 수록 counter 값은 높을 수록 우선순위가 높음
  우선순위가 가장 높은 proces를 찾기 위해 O(n) 성능을 보임
list_for_each(tmp, &runqueue_head)
{
p = list_entry(tmp, struct task_struct, run_list);
if (can_schedule(p, this_cpu))
{
int weight = goodness(p, this_cpu, prev->active_mm);
if (weight > c)
c = weight, next = p;
}
}
...
weight = p->counter; // time slice
weight += 20 - p->nice;

## Slide 15
0
100
10
50
-10
150
-5
125
nice
counter
우선순위 계산 공식
weight = counter + 20 - nice
120
180
60
150
prev
next
tasks

## Slide 16
2세대 커널
  Bitmap과 hash를 이용한 검색 방식
  Bitmap을 사용 하여 상수 시간내의 검색 가능
  우선순위가 가장 높은 proces를 찾기 위해 O(1) 성능을 보임
idx = sched_find_first_bit(array->bitmap);
queue = array->queue + idx;
next = list_entry(queue->next, task_t, run_list);
if (unlikely(!array->nr_active))
{
schedstat_inc(rq, sched_switch);
rq->active = rq->expired;
rq->expired = array;
array = rq->active;
rq->expired_timestamp = 0;
rq->best_expired_prio = MAX_PRIO;
}

## Slide 17
2세대 커널
RT Process : 0 ~ 99
nice : -20 ~ 19 => 100 ~ 139
1
1
1
1
1
1
[0]
[1]
[2]
[3]
[4]
find_next_set_bit();
100
O(1)

## Slide 18
1
1
1
[0]
[1]
[2]
[3]
[4]
100
[0]
[1]
[2]
[3]
[4]
100
active
expired
array
0
nr_active
rq->active = rq->expired;
rq->expired = array;
array = rq->active;

## Slide 19
2세대 커널의 문제점
  CFS 출현 배경
  1. 스케쥴 단위가 우선순위에 의해서 결정 되면 안된다.
  nice=0 , 2개 실행 100ms, 100ms
  nice=19, 2개 실행 100ms, 100ms
  2. 우선순위의 단계별 비율이 일정 하지 않다.
  nice=0, nice=1 100ms(51.2%), 95ms(48.8%)
  nice=18, nice=19 10ms(66.6%), 5ms(33.3%)
  3. 낮은 우선순위의 프로세스는 상황에 따라 기아 상태가 될 수 있다.
  I/O 전용 프로세스 10 개 실행중
  계산 전용 프로세스 1 개 실행 중

## Slide 20
const int sched_prio_to_weight[40] = {
/* -20 */ 88761, 71755, 56483, 46273, 36291,
/* -15 */ 29154, 23254, 18705, 14949, 11916,
/* -10 */ 9548, 7620, 6100, 4904, 3906,
/* -5 */ 3121, 2501, 1991, 1586, 1277,
/* 0 */ 1024, 820, 655, 526, 423,
/* 5 */ 335, 272, 215, 172, 137,
/* 10 */ 110, 87, 70, 56, 45,
/* 15 */ 36, 29, 23, 18, 15,
};

## Slide 21
nice | weight | w/weight | slice(ns) | w0/w | vruntime
-10 | 9548 | 0.68 | 4052058 | 0.1072476 | 434573.49
-5 | 3121 | 0.22 | 1324515 | 0.3281 | 434573.49
0 | 1024 | 0.07 | 434573 | 1 | 434573.49
5 | 335 | 0.02 | 142170 | 3.0567164 | 434573.49
10 | 110 | 0.01 | 46683 | 9.3090909 | 434573.49
total | 14138 | 1 | 6000000 |  | 
nice | weight | w/weight | slice(ns) | w0/w | vruntime
-10 | 9548 | 0.68 | 5000000 | 0.1072476 | 536237.96
-5 | 3121 | 0.22 | 1324515 | 0.3281 | 434573.49
0 | 1024 | 0.07 | 434573 | 1 | 434573.49
5 | 335 | 0.02 | 142170 | 3.0567164 | 434573.49
10 | 110 | 0.01 | 20000 | 9.3090909 | 186181.82
total | 14138 | 1 | 6000000 |  | 

## Slide 22
2세대 커널의 문제점
  CFS 출현 배경
  1. 스케쥴 단위가 우선순위에 의해서 결정 되면 안된다.
  nice=0 , 2개 실행 100ms, 100ms
  nice=19, 2개 실행 5ms, 5ms
nice | weight | w/weight | slice(ns) | w0/w | vruntime
0 | 1024 | 0.50 | 3000000 | 1 | 3000000
0 | 1024 | 0.50 | 3000000 | 1 | 3000000
total | 2048 | 1 | 6000000 |  | 
nice | weight | w/weight | slice(ns) | w0/w | vruntime
19 | 15 | 0.50 | 3000000 | 1 | 3000000
19 | 15 | 0.50 | 3000000 | 1 | 3000000
total | 30 | 1 | 6000000 |  | 

## Slide 23
2세대 커널의 문제점
  CFS 출현 배경
  2. 우선순위의 단계별 비율이 일정 하지 않다.
  nice=0, nice=1 100ms(51.2%), 95ms(48.8%)
  nice=18, nice=19 10ms(66.6%), 5ms(33.3%)
"10% effect"
const int sched_prio_to_weight[40] = {
/* -20 */ 88761, 71755, 56483, 46273, 36291,
/* -15 */ 29154, 23254, 18705, 14949, 11916,
/* -10 */ 9548, 7620, 6100, 4904, 3906,
/* -5 */ 3121, 2501, 1991, 1586, 1277,
/* 0 */ 1024, 820, 655, 526, 423,
/* 5 */ 335, 272, 215, 172, 137,
/* 10 */ 110, 87, 70, 56, 45,
/* 15 */ 36, 29, 23, 18, 15,
};

## Slide 24
nice | weight | w/weight | slice(ns) | w0/w | vruntime
-10 | 9548 | 0.68 | 5000000 | 0.1072476 | 500000
-5 | 3121 | 0.22 | 1324515 | 0.3281 | 400000
0 | 1024 | 0.07 | 434573 | 1 | 300000
5 | 335 | 0.02 | 142170 | 3.0567164 | 200000
10 | 110 | 0.01 | 20000 | 9.3090909 | 100000
total | 14138 | 1 | 6000000 |  | 
3
2
5
1
4
next
O(log2N)
cfs_rq
rb_leftmost
tasks_timeline

## Slide 25
task_struct
se
vruntime
run_node
next

## Slide 26
current process의 vruntime update 시점
tick_periodic()
update_process_times();
scheduler_tick();
curr->sched_class->task_tick(rq, curr, 0);
task_tick_fair();
entity_tick(cfs_rq, se, queued);
update_curr(cfs_rq);
u64 now = rq_clock_task(rq_of(cfs_rq));
delta_exec = now - curr->exec_start
curr->vruntime += calc_delta_fair(delta_exec, curr);
if (unlikely(se->load.weight != NICE_0_LOAD))
delta = __calc_delta(delta, NICE_0_LOAD, &se->load);
fact = (u64)(u32)fact * lw->inv_weight; // 커널모드에서는
// 부동소수점을 지원하지 않는다.
while (fact >> 32) {
fact >>= 1;
shift--;
}

## Slide 27
const int sched_prio_to_weight[40] = {
/* -20 */ 88761, 71755, 56483, 46273, 36291,
/* -15 */ 29154, 23254, 18705, 14949, 11916,
/* -10 */ 9548, 7620, 6100, 4904, 3906,
/* -5 */ 3121, 2501, 1991, 1586, 1277,
/* 0 */ 1024, 820, 655, 526, 423,
/* 5 */ 335, 272, 215, 172, 137,
/* 10 */ 110, 87, 70, 56, 45,
/* 15 */ 36, 29, 23, 18, 15,
};
Inverse (2^32/x) values
const u32 sched_prio_to_wmult[40] = {
/* -20 */ 48388, 59856, 76040, 92818, 118348,
/* -15 */ 147320, 184698, 229616, 287308, 360437,
/* -10 */ 449829, 563644, 704093, 875809, 1099582,
/* -5 */ 1376151, 1717300, 2157191, 2708050, 3363326,
/* 0 */ 4194304, 5237765, 6557202, 8165337, 10153587,
/* 5 */ 12820798, 15790321, 19976592, 24970740, 31350126,
/* 10 */ 39045157, 49367440, 61356676, 76695844, 95443717,
/* 15 */ 119304647, 148102320, 186737708, 238609294, 286331153,
};

## Slide 28
#include <stdio.h>
#include <stdlib.h>
#include <pthread.h>
void *foo(void *data)
{
printf("\t\tchild\n");
return 0;
}
int main()
{
pthread_t thread;
pthread_create(&thread, 0, foo, 0);
pthread_join(thread, 0 );
printf("parent\n");
return 0;
}
#include <stdio.h>
#include <unistd.h>
#include <stdlib.h>
#include <sys/wait.h>
int main()
{
pid_t pid;
pid = fork();
if( pid == 0 )
{
printf("\t\tchild\n");
exit(0);
}
wait(0);
printf("parent\n");
return 0;
}
process
thread

## Slide 29
process
thread
공통점 : 스케줄 단위 이다. (동시성 보장)
fork()
----------
sys_fork();
_do_fork();
...
pthread_create();
clone();
----------
sys_clone();
_do_fork();
...

## Slide 30
process
thread
차이점 : 전체 가상메모리의 공유 유/무
fork()
----------
sys_fork();
_do_fork(SIGCHILD);
...
pthread_create();
clone();
----------
sys_clone();
_do_fork(CLONE_VM);
...

## Slide 31
mm
mmap
vm_start
vm_end
parent
mm
child
mmap
vm_start
vm_end

## Slide 32
mm
2
mmap
vm_start
vm_end
parent
mm
child

## Slide 33
0000000001 0000000000 010000000000
0
0
0
0
0
0
0
0
0
1
0
0
0
0
0
0
0
0
0
0
0
1
0
0
0
0
0
0
0
0
0
0
CPU
pgd
[1]
1
pte
[0]
pud
pmd
0x00400400
0x0000
0x1000
0x2000
0x3000

## Slide 34
0000000001 0000000000 010000000000
0
0
0
0
0
0
0
0
0
1
0
0
0
0
0
0
0
0
0
0
0
1
0
0
0
0
0
0
0
0
0
0
pgd
[1]
1
3
pte
[0]
pud
pmd
0x00400000
0x00401000
0x0000
0x1000
0x2000
0x3000
0000000001 0000000001
[1]

## Slide 35
0000 0000 0100 00000000 010000000000
0
0
0
0
0
0
0
0
0
1
0
0
0
0
0
0
0
0
0
0
0
1
0
0
0
0
0
0
0
0
0
0
pgd
[1]
1
3
pte
[0]
pud
pmd
0x00400000
0x00800000
0x0000
0x1000
0x2000
0x3000
0000 0000 1000 00000001
[1]
[2]
pte

## Slide 36
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
0
0
0
0
0
0
0
0
0
0
0
0
0
0
1
0
1
2
3

## Slide 37
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
0
0
0
1
0
0
0
0
0
1
0
0
1
0
0
0
1
2
3
p1 = __get_free_pages(0);

## Slide 38
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
0
0
0
0
0
0
0
0
0
1
0
0
1
0
0
0
1
2
3
p2 = __get_free_pages(0);

## Slide 39
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
0
0
1
0
0
0
0
0
0
0
0
0
1
0
0
0
1
2
3
p3 = __get_free_pages(0);

## Slide 40
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
0
0
1
1
0
0
0
0
0
0
0
0
1
0
0
0
1
2
3
free_pages(0, p2);

## Slide 41
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
0
0
0
1
0
0
0
0
0
1
0
0
1
0
0
0
1
2
3
free_pages(0, p3);

## Slide 42
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
0
0
0
0
0
0
0
0
0
0
0
0
0
0
1
0
1
2
3
free_pages(0, p1);